## Slide 1
PITCH-A-BOT
DELIVERY BOX
MAHESH GHUMARE

## Slide 2
UNDERSTANDING THE PROBLEM
The given problem wants us to design a box which can be installed outside our main door so that the delivery boy could keep our parcel inside this box.
This box is to be devised such that after we lock it, it should generate a 5-digit key and send it to the owner via Email or SMS. So that, if the owner is unable to receive his/her order personally, the automated delivery box will receive it and keep it safe.

## Slide 3
IDEA AND APPROACH
This can be done by programming a micro-controller such that it would generate a key ,send it to the owner and lock itself. So that delivery box can could only be opened by this very same key it generated. Every time we lock our delivery box, it should generate a new key.
To do this we will be using a set of buttons (4X4 Keypad) placed on this box and a display visible above keypad. Every Button will have there own functioning . For example if we pressed a key named ‘A’ on keypad we should enter the generated key and if we press a key named ‘B’ on keypad the box should generate new key, send it to the owner and lock delivery box.

## Slide 4: COMPONENTS REQUIRED
ESP8266 NodeMcu
16X2 LCD DISPLAY WITH I2C BUS
4X4 KEYPAD
SERVO MOTOR
WIRES
TOWER BOLT

## Slide 5: CIRCUIT DIAGRAM
As the command to lock the delivery box is given ,the servo will rotate by 120 degrees which will be connected to tower bolt with non bending rod like structure which will push the tower bolt into the lock mode.

## Slide 6
TOP VIEW OF DELIVERY BOX
Just to show how input/output look like on the box

## Slide 7: PSEUDOCODE
If pressed ‘A’ on keypad :
check key , unlock if key is correct , display “CORRECT/INCORRECT”
If pressed ‘B’ on keypad:
generate new key , send key to the owner , display “key generating/generated”

## Slide 8: TAKEAWAY AND RESOURCES
-Connections required for an LCD with I2C bus
https://www.youtube.com/watch?v=2Z3w4VfdlFM
-Working with Servo
https://www.youtube.com/watch?v=tlgLA-PT5eE
-Working with keypads
https://www.youtube.com/watch?v=8_oz_0m_KN4
-Connecting to WiFi
https://www.youtube.com/watch?v=uwjWyMFwvQw

## Slide 9: THANKS